## Slide 1
Computer Network
Lab 3
Rehab Hosny

## Slide 2: Number of hosts per classes
Class | Default mask | Hosts | 
Class A | 255.0.0.0 | 16777217 | 
Class B | 255.255.0.0 | 65534 | 
Class C | 255.255.255.0 | 254 | 

## Slide 3: Types of Message
. Unicast: in a single destination between switch or router to one device (host) this mean one-to-one.
. Multicast: the packet sends from single source to many hosts in the network this mean one-to-many.
. Broadcast: the packet sends from single source to all hosts this mean one –to-all.

## Slide 4: Custom Mask
this method allow us to use number of hosts that responds our need.

## Slide 5: How we calculate custom Mask?
Suppose we have 500 hosts in network, what is suitable subnet mask used?
We use (2^h - 2 ) =number of hosts
So, 2^9 – 2= 510
Then h= 9
Number of zeros in custom mask from right are 9, so custom mask that suitable to this network is
11111111.11111111.11111110.00000000
255.255.254.0

## Slide 6: How we calculate custom Mask? (Cont.)
Suppose we have 2000 hosts in network.
Step 1:
We use the equation (2^h-2) to execute the number of zeros in the subnet mask.
The nearest number of 2000is 2048
2^11 -2=2046.
Then h= 11 (the number of zeros).

## Slide 7: How we calculate custom Mask? (Cont.)
Step 2:
The subnet is in binary 11111111.11111111.11111000.00000000
In decimal
255.255.248.0

## Slide 8: How we calculate custom Mask? (Cont.)
Step 3:
We take a random IP 10.80.80.80
convert it to binary
00001010.01010000. 01010000. 01010000

## Slide 9: How we calculate custom Mask? (Cont.)
Step 4:
We make AND operation between the random IP and subnet mask to extract the subnet in our network. 11111111.11111111.11111000.00000000
00001010.01010000.01010000.01010000
The result is:
00001010. 01010000. 01010000.00000000
10.80.80.0

## Slide 10: How we calculate custom Mask? (Cont.)
How to calculate Broadcast IP?
11111111.11111111.11111000.00000000
00001010.01010000.01010000.01010000
Broadcast IP is 00001010.01010000.01010111.11111111
10.80.87.255

## Slide 11: How we calculate custom Mask? (Cont.)
This Custom Mask 255.255.248.0 include 2048 Hosts

## Slide 12
END