## Slide 1: Computer Network Lab 5

## Slide 2: Virtual LANs (VLANs)
Allow us to split switches into separate (virtual) switches
Edge ports, where end nodes are connected, are configured as members of a VLAN
VLANs are assigned to switch ports. There is no “VLAN” assignment done on the host (usually).

## Slide 3: VLAN operation
As a device enters the network, it automatically assumes the VLAN membership of the port to which it is attached.
The default VLAN for every port in the switch is VLAN 1 and cannot be deleted.

## Slide 4: VLANs across switches
Two switches can exchange traffic from one or more VLANs
Inter-switch links are configured as trunks, carrying frames from all or a subset of a switch’s VLANs
Each frame carries a tag that identifies which VLAN it belongs to

## Slide 5: VLAN Connections
During the configuration of VLAN on port, we need to know what type of connection it has.
Switch supports two types of VLAN connection
  Access link
  Trunk link

## Slide 6: VLAN Connections
Access link
Access link connection is the connection where switch port is connected with a device
Trunk link
Trunk link connection is the connection where switch port is connected with a device that is capable to understand multiple VLANs

## Slide 7
END