## Slide 1: Introduction To Wireless Communications and Networks
Dr.Mohammed Abdalla Youssif
IT Department
1

## Slide 2: OUTLINE
BACKGROUND
Location based services : aim
Predictive Spatial Queries: Definition
Predictive Spatial Queries: Common types
Predictive Queries: Applications
Predictive Spatio-Temporal Query
Spatio-temporal Data Management : Open Research Areas
Challenges
Conclusions
2
Notes: 2

## Slide 3: BACKGROUND
Wireless Communications
  Responsibility: Communication engineers
  Physical layer
  Data link layer
Networks
  Responsibility: Software Engineers
  Application layer
  Network Layer
  Transport Layer
3
Notes: Wireless Communications and networks – William Stallings
3

## Slide 4: BACKGROUND
What is the role of each layer:
  Application layer
  Network Layer
  Transport Layer
  Data link layer
  Physical layer
4
Notes: Wireless Communications and networks – William Stallings
4

## Slide 5: Wireless Comes of Age
Guglielmo Marconi invented the wireless telegraph in 1896
  Communications by encoding alphanumeric characters in analog signals
  Sent telegraphic signals across Atlantic ocean
Communications satellites launched in 1960s
Advances in wireless technology
  Radio,television,mobiletelephone,communication satellites
More Recently
  Satellite communications, wireless networking, cellular technology
5
Notes: 5

## Slide 6: Broadband Wireless Technology
Higher data rates obtainable with broadband wireless technology
  Graphics, video, audio
Share same advantages of all wireless services: convenience and reduced cost
  Service can be deployed faster
  No cost of cable
  Service is mobile, deployed almost anywhere.
6
Notes: Boradband هو البث على نطاق واسع وعدة نطاقات وليس نطاق واحد
وبث مجموعة من الاشارات فى نفس الوقت
6

## Slide 7: Three Faces of Networking
Fundamental concepts of networking
  How data moves from one computer to another over a network
  Theories of how network operate
Technologies in use today
  How theories are implemented, specific products
  How do they work, their use, applications
Management of networking technologies
  Security
  Network Design
  Managing the network

## Slide 8: Topics Coverage
Data Communications
TCP/IP
8
Notes: Boradband هو البث على نطاق واسع وعدة نطاقات وليس نطاق واحد
وبث مجموعة من الاشارات فى نفس الوقت
8

## Slide 9: DEFNTION
Data communications (DC) is the process of using communication technologies to transfer data from one place to another, and vice versa.
It enables the movement of electronic or digital data between two or more nodes, regardless of geographical location, technological medium or data contents.
Common example of data communications is a computer connected to the Internet via a Wi-Fi connection, which uses a wireless medium to send and receive data from one or more remote servers.
9
Notes: 9

## Slide 10: DEFNTION
10
Notes: 10

## Slide 11: Effectiveness of data Communication
The Effectiveness of data communication depends on three fundamental characteristics
11
Notes: Delivery : system must deliver data to correct destination
Accuracy :system must deliver correct data.
Timeliness : system must deliver data in reasonable time
11

## Slide 12: Communications Tasks
Transmission system utilization | Addressing
Interfacing | Routing
Signal generation | Recovery
Synchronization | Message formatting
Exchange management | Security
Error detection and correction | Network management
Flow control | 

## Slide 13: Components of Data Communication
13
Notes: Message
Sender
Receiver
Protocols: set of rules for data communication
Transmission link : physical link between sender and receiver.
13

## Slide 14: Topology
How To connect 2 or More devices ? Topology
Two or more devices connect to a link and two or more links form topology.
14
Notes: 14

## Slide 15: Types of Topology
Bus Topology
Star Topology
Ring Topology
Mesh Topology
15
Notes: 15

## Slide 16: Bus Topology
Bus topology is a specific kind of network topology in which all of the various devices in the network are connected to a single cable or line.
16
Notes: 16

## Slide 17: Star Topology
Set or more devices connected to central Hub
The major disadvantage is if the central hub fail all devices will be disconnected.
17
Notes: 17

## Slide 18: Ring Topology
computer network configuration which each device connect to each other forming circle.
Each packet is go to around until it reaches final destination.
18
Notes: 18

## Slide 19: Mesh Topology
Each computer and network device is interconnected with one another, allowing for most transmissions to be distributed, even if one of the connections go down.
19
Notes: 19

## Slide 20: A Communications Model
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data

## Slide 21: Communications Tasks
Transmission system utilization | Addressing
Interfacing | Routing
Signal generation | Recovery
Synchronization | Message formatting
Exchange management | Security
Error detection and correction | Network management
Flow control | 

## Slide 22
  We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Layered Tasks

## Slide 23
Figure Tasks involved in sending a letter

## Slide 24
  Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
The OSI Model

## Slide 25
Figure Seven layers of the OSI model

## Slide 26
2-3 LAYERS IN THE OSI MODEL
  In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed :

## Slide 27
Figure 2.5 Physical layer

## Slide 28
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 29
Figure Data link layer

## Slide 30
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 31
Figure 2.8 Network layer

## Slide 32
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 33
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 34
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 35
Figure 2.12 Session layer

## Slide 36
The session layer is responsible for dialog control and synchronization.
Note

## Slide 37
Figure 2.13 Presentation layer

## Slide 38
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 39
The application layer is responsible for providing services to the user.
Note

## Slide 40: Layer 1: Physical Layer
Responsible of:
  Transmitting individual bits from one to the next.
  Physical characteristics of interface and media.
  Representation of bits: a stream of bit(0s,1s),
  Data rate.
  Synchronize of bits
  Line configuration
  Physical topology
  Transmission mode

## Slide 41: Physical Layer cont.

## Slide 42: Layer 2: Data Link layer
Responsible of:
  Moving frames from one hop (node) to the next.
  Framing: divided the stream of bits received from the network layer manageable data units called frames.
  Physical address (MAC address).
  Flow control.
  Error control: added trailer to the end of frame.
  Access control.
  Hop to hop delivery

## Slide 43: Data Link layer cont.
10110110101
01100010011
10110000001

## Slide 44: Hop-to-Hop delivery

## Slide 45: Layer 3: Network Layer
The network layer is responsible:
  The delivery of individual packets from the original source to the final destination .
  Logical addressing: if the packet passes the network boundary we need another addressing system to help (source to destination) connection.
  Routing : route or switch the packet to final destination.
  Source-to-destination delivery (End-to-End).

## Slide 46: Network Layer cont.

## Slide 47: Source-to-Destination delivery

## Slide 48: Layer 4: Transport Layer
The transport layer is responsible for:
  Service point or Port addressing
  Segmentation and reassembly : a message is divided into transmittable segments each segment containing a sequence no.
  Connection Control: connection oriented or connectionless.
  Flow control
  Error control

## Slide 49: Transport Layer cont.

## Slide 50: Reliable process-to-process delivery of a message

## Slide 51: Layer 5: Session Layer
Dialog control: design to establish, maintain, and synchronize the interaction between communicating systems.
Synchronization: it allows a process to add checkpoints or synchronization points to a data stream.

## Slide 52: Session Layer cont.

## Slide 53: Layer 6 :Presentation Layer
Design to the handle the syntax and semantic of the information exchanged between 2 systems.
And design for data translation, encryption, decryption, and compression.

## Slide 54: Presentation Layer cont.

## Slide 55: Layer 7: Application Layer
The application layer is responsible for providing services to the user.
Mail services
File transfer, access and management
Remote log-in or network virtual terminal
Accessing the World Wide Web
Directory service

## Slide 56: Application Layer cont.
HTTP
Telnet
SMTP
HTTP
Telnet
SMTP

## Slide 57: Summary

## Slide 58
Figure 2.15 Summary of layers

## Slide 59
2-5 ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.
Physical Addresses Logical Addresses Port Addresses Specific Addresses
Topics discussed in this section:

## Slide 60
Figure 2.17 Addresses in TCP/IP

## Slide 61
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 62
DEVICES :
Hub, a distributor that has a lot of ports which connected to computers.
Switches, like a hub but it transmit packets to it destination
Bridge, it is used to connect two similar LANs.
Routers, choose the best path to transmit the packet.
Gateway, it is use to connect two deferent LANs and connect different application protocols.
Repeaters, repeats signals that travels via long distance

## Slide 63: Network devices With Layer
Layers | Network Devices
Application Layer | Application gateway
Transport Layer | Transport gateway
Network Layer | Router and gateway
Data link layer | Bridge and Switch
Physical Layer | Repeater, Hub and Modem.

## Slide 64: Questions ?
64
Notes: 64