## Slide 1: Chapter 2 Transmission Fundamentals
Dr.Mohammed Abdalla Youssif
1

## Slide 2: Electromagnetic Signal
Function of time
Can also be expressed as a function of frequency
  Signal consists of components of different frequencies.
2
Notes: Wireless Communications and networks – William Stallings
2

## Slide 3: Time-Domain Concepts
Analog signal: signal intensity varies in a smooth fashion over time
  No breaks or discontinuities
Digital signal: signal intensity maintains a constant level for some period of time and then changes to another constant level.
Periodic Signal: analog or digital signal pattern that repeats over the time.
3
Notes: 3

## Slide 4: Time-Domain Concepts
Aperiodic Signal: analog or digital signal pattern that does not repeat over the time
Peak amplitude (A): a maximum value or strength of the signal over time, typically measured in volts.
Frequency(F): Rate, in cycles per second, or Hertz(Hz) at which the signal repeats.
4
Notes: 4

## Slide 5: Time-Domain Concepts
Period (T): amount of time it takes for one repetition of the signal T=1/F
Phase() - ) –measure of the relative position in time within a single period of a signal.
Wavelength( ) – distance occupied by a single cycle of the signal.
  Or, the distance between two points of corresponding phase of two consecutive cycles.
5
Notes: 5

## Slide 6: Periodic Signal Example
6
Notes: 6

## Slide 7: Sine Wave Parameters
General Sine Wave
The next figure shows the effect of varying each of the three parameters (amplitude, frequency, phase):
Note:
7
Notes: 7

## Slide 8: Case 1
Parameters: Amplitude =1, Frequency=1, phase=0
8
Notes: 8

## Slide 9: Case 2
Parameters: Amplitude =0.5, Frequency=1, phase=0
9
Notes: 9

## Slide 10: Case 3
Parameters: Amplitude =1, Frequency=2, phase=0
10
Notes: 10

## Slide 11: Case 4
Parameters: Amplitude =1, Frequency=2, phase=0
11
Notes: 11

## Slide 12: Time VS. Distance
When the horizontal axis is time, as shown in the pervious figure, the graph displays the value of a signal at a given point in space as a function of time.
With horizontal axis in space, graph displays the value of a signal at a given point in time as function of distance
  At a particular instant of time, the intensity of the signal varies as a function of distance from the source.
12
Notes: 12

## Slide 13: Frequency-Domain Concepts
Fundamental frequency – when all frequency components of a signal are integer multiples of one frequency, it’s refereed to as the fundamental frequency
Spectrum – range of frequencies that a signal contains
Absolute bandwidth- width of the spectrum of signal
Effective bandwidth (or just bandwidth) – narrow band of frequencies that most of signal’s energy is contained in.
13
Notes: 13

## Slide 14: Frequency-Domain Concepts
Any electromagnetic signal can be shown to consists of a collection of periodic analog signals (sine waves) at different amplitudes, frequencies, and phases
The period of the total signal is equal to the period of the fundamental frequency.
14
Notes: 14

## Slide 15: Data Communication Terms
Data – entities that convey meaning, or information
Signals – electric or electromagnetic representations of data., Signals can be analog or digital.
  Examples of analog data: video and audio
  Examples of digital data : text
Transmission – communication of data by the propagation and processing of signals
15
Notes: convey نقل
15

## Slide 16: Analog signals
A continuously varying electromagnetic wave that may be propagated over a variety of media, depending on the frequency.
Analog signals can propagate analog and digital data
16
Notes: convey نقل
16

## Slide 17: Analog signals
17
Notes: convey نقل
17

## Slide 18: Digital signals
A sequence of voltage pulses that may be transmitted over a copper wire medium
Generally cheaper than analog signaling
Less susceptible to noise interference
Suffer more from attenuation
Digital signals can propagate analog and digital data.
18
Notes: convey نقل
18

## Slide 19: Digital signals
19
Notes: convey نقل
19

## Slide 20: Reasons for Choosing Data and Signal Combinations
Digital data, digital signal
  Equipment for encoding is less expensive than digital-to-analog equipment
Analog data, digital signal
  Conversion permits use of modern digital transmission and switching equipment
Digital data, analog signal
  Some transmission media will only propagate analog signals
  Examples include optical fiber and satellite
Analog data, analog signal
  Analog data easily converted to analog signal
20
Notes: convey نقل
20

## Slide 21: Analog Transmission
Transmit analog signals without regard to content
Attenuation limits length of transmission link
Cascade amplifiers boost signal’s energy for longer distances but cause distortion
  Analog data can tolerate distortion
  Introduces errors in digital data.
21
Notes: convey نقل
21

## Slide 22: Digital Transmission
Concerned with the content of the signal
Attenuation endangers integrity of data
Digital Signal
  Repeaters achieve greater distance
  Repeaters recover the signal and retransmit
Analog signal carrying digital data
  Retransmission device recovers the digital data from analog signal
  Generate new, clean analog signal.
22
Notes: convey نقل
22

## Slide 23
23
Notes: convey نقل
23

## Slide 24
24
Notes: convey نقل
24

## Slide 25
25
Notes: 25

## Slide 26
26
Notes: 26

## Slide 27
27
Notes: 27

## Slide 28
28
Notes: 28

## Slide 29
29
Notes: 29

## Slide 30
30
Notes: 30

## Slide 31
31
Notes: 31

## Slide 32
32
Notes: 32

## Slide 33
33
Notes: 33

## Slide 34
34
Notes: 34

## Slide 35
35
Notes: 35

## Slide 36
36
Notes: 36

## Slide 37
37
Notes: 37

## Slide 38
38
Notes: 38

## Slide 39
39
Notes: 39

## Slide 40
40
Notes: 40

## Slide 41: Questions ?
41
Notes: 41